Quasi Free Scattering Analysis with Experiment S444/467 (2020)
12C(p,2p)11B reaction:
SETUP:
Beam energy: 400 AMeV
Beamtype: 12C
Target: CH2
2 protons
11B fragment
(spectator)
12C beam
proton like target
proton
11B
proton

---
Fragment Particle Identification
Flightpath reconstruction:
12C
11C
Radius reconstruction:
size*1 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
10B
11B
size*1.5 {B*%rho " " = " "{{%beta*%gamma*M} over {q}}}

---
12C(p,2p)11B reaction
Two Proton Identification:
→ two hits with Ehit > 30 MeV
proton
proton

---
Gamma Spectrum of 11B
laboratory system
Doppler Correction:
size*1.5 E_{ %gamma } = size*1.5 %gamma size*1.5E_{ lab} size*1.5( 1- %beta cos (%theta ))
11B rest frame
2.1 MeV (1/2-) p-hole state
5.0 MeV (3/2-) p-hole state
+ single/double escape

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
y
φ
x
φ1[degrees]
Tobias Jenegger
φ2[degrees]

---
Gamma Spectrum with Angular Cuts
Event selection criteria for CALIFA:
→ 11B fragment identification
→ two hits (protons) with Ehit > 30 MeV
→ θ1 + θ2 < 90°
→ Δφ = 180° +- 40°
TODO: make bkg from 1 to 3 and add also plots with hit-multiplicities...

---
Reconstruction of Inner Momenta
pi
p1
p2
ptg
11B
11B
Momentum conservation relation:
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
assuming QE scattering in mean field potential:
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
nucleon momentum inside 12C
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5 abs{ vec{p_i} }

---
Momentum components of p_i
pi
p1
p2
Momentum conservation relation:
ptg
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
11B
assuming QE scattering in mean field potential:
11B
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
momentum-components (with angular cuts applied)
z-comp
y-comp
x-comp
size*1.5 abs{ vec{p_i} }

---
Missing Energy Distribution
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5{E_miss " " = " " m_p - e_miss }
11B
(where e_miss is the energy component of pmissing)
Emiss can be interpreted as
E_sep + E_mean_exc:
Emiss = Efinal -Einitial
Emiss = Etgkin + mtg + mp – mp1 -Ep1kin – mp2 -Ep2kin
(where mp = mtg = mp1 = mp2 as they are all protons)
Emiss = Etgkin -Ep1kin – Ep2kin (in 12C cms)
This was without angular cut (theta_sum < 90° and phi1+phi2 = 180° +- 40°)
pi
ptg
11B
p2
p1

---
Missing Energy Distribution
Now with cut on angles: theta_sum < 90° and phi_diff = 180° +- 40°
But how can this prominent edge be explained?

---
Analysis Missing Energy Distribution
Explicit calculation of the Missing Energy (in the 12C frame):
Emiss = Etgkin -Ep1kin – Ep2kin
size*1.2{ E_miss = 400 - ( %gamma*(E_kin1+938) - %gamma*%beta*sqrt{(E_kin1+938)^2 -938^2}*cos(%theta_1) -938 ) - ( %gamma*(E_kin2+938) - %gamma*%beta*sqrt{(E_kin2+938)^2 -938^2}*cos(%theta_2) -938 )}
E_potp1
E’p1
E_potp2
E’p2
Etgkin
Ekin2
Ekin1

---
E_missing and p_z_missing for different opening angles
For simplicity let’s say θ1 = θ2. That means for theta_sum = 44 ° → θ1 = θ2 = 22°
Maximum ≈ 270 MeV

---
E_missing and p_z_missing for θ1 = θ2 = 41°
Maximum ≈ 20 MeV

---
Mass reconstuction of p_i
pi
p1
p2
ptg
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5{M_i = sqrt{(bold{p_1} + bold{p_2} - bold{p_tg})^2} }
11B
11B
Looks ok, mean of 918 MeV is lower than expected….
size*1.5 abs{ vec{p_i} }

---
Momentum p_i vs p_11B in 12C
With y-information from MW1 and MW2
Now with y-info from MW1 and MW3
p_x ≈ p_y

---
Missing mass reconstruction
pi
p1
p2
ptg
11B
size*1.5{M_miss = sqrt{(p_12C - p_i - p_11B)^2} }
11B
should be ≈ 0
→ give better look at the 3- momentum distribution
(+- permutation at MW position??)
→ as the reconstruction of p_i works well it can be deduced that 11B reconstruction faulty….
???
size*1.5 abs{ vec{p_i} }

---
Inner angular distributions
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
In 12C cms frame (using MW1 and MW2) :
Not satisfactory….
See: https://www.nature.com/articles/s41567-021-01193-4.pdf
Here I plotted the angle between the 3D vectors pi and p11B
This is the angle in the x-y plane

---
Angular Distribution in x-y plane
Therefore the y position was determined using MWPC3
The y-position of MWPC3 has been reversed (meaning +y→-y and -y→+y)
GREAT!

---
Excitation Energy of 11B
size*2{ E_exc = (bold{P_12C + p_tg - p_1 -p_2}).M -M_11B }
-pi
Is this formula valid?

---
Correlation between knocked out proton and 11B
This is with Py_fragment reconstruction from MW1 and MW3
With given formula:
This plot was with Py_fragment reconstruction from MW1 and MW2

---
Correlation between knocked out proton and 11B
What we expect:
experiment
simulation

---
Explanation of
Is a Cartesian component of the internal momentum of the internal momentum of the knocked out proton from 12C perpendicular to the reaction plane.
The reaction plane is given by the 12C momentum vector and the scattered target proton.
Can be plotted also against Px_fragment (see next slide). This is a blurred centered spot. This can be explained by:
→ acceptance of CALIFA: no crystals in the phi +-90° region , therefore the y component is dominant
→ low precision for y position (can be partly solved using MW1.Y vs MW3.Y, but then straggling..)
For more details and derivation see: https://www.sciencedirect.com/science/article/abs/pii/S0375947405008523

---
12C(p,ppn/pd)10B Reaction
or

---
First Angular and Momentum Plots ...
Without cut:

---
Reconstruction of inner momentum p_i
size*1.5 {abs{ vec{p_i} } " " (MeV/c)}
size * 1.5 {bold{p_{ i }} = ( bold{p_{1} + p_{1} - p_tg } )}

---
Neutron Mass Reconstruction
???
before reaction
after reaction
size * 1.5 {M²_{ missing } = ( bold{p_{12C} + p_{tg} - p_1 - p_2 - p_{10B}} )^2}