Quasi Free Scattering with S444 data
Tobias Jenegger
Analysis WG Meeting
22.07.2021
12C(p,2p)11B reaction
12C(p,ppn/pd)10B reaction
SRC Analysis
Supported by BMBF 05P15WOFNA and 05P19WOFN1.
The results presented here are based on the experiment s444/s473, which was performed at the beam line/infrastructure Cave C at the GSI Helmholtzzentrum für Schwerionenforschung, Darmstadt (Germany) in the frame of FAIR Phase-0.
Physics with R3B
CALIFA – Design

---
Quasi Free Scattering Analysis with Experiment S444/467 (2020)
12C(p,2p)11B reaction:
SETUP:
Beam energy: 400 AMeV
Beamtype: 12C
Target: CH2
2 protons
11B fragment
(spectator)
12C beam
proton like target
proton
11B
proton

---
Fragment Particle Identification
Flightpath reconstruction:
12C
11C
Radius reconstruction:
size*1 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
10B
11B
size*1.5 {B*%rho " " = " "{{%beta*%gamma*M} over {q}}}

---
12C(p,2p)11B reaction
Two Proton Identification:
→ two hits with Ehit > 30 MeV
proton
proton

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
y
φ
x
φ1[degrees]
Tobias Jenegger
φ2[degrees]

---
Gamma Spectrum of 11B
laboratory system
Doppler Correction:
size*1.5 E_{ %gamma } = size*1.5 %gamma size*1.5E_{ lab} size*1.5( 1- %beta cos (%theta ))
11B rest frame
2.1 MeV (1/2-) p-hole state
5.0 MeV (3/2-) p-hole state
+ single/double escape

---
Gamma Spectrum with Angular Cuts
Event selection criteria for CALIFA:
→ 11B fragment identification
→ two hits (protons) with Ehit > 30 MeV
→ θ1 + θ2 < 90°
→ Δφ = 180° +- 40°
TODO: make bkg from 1 to 3 and add also plots with hit-multiplicities...

---
Reconstruction of Inner Momenta
After Scattering:
(Four-)Momentum conservation relation:
p11B
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
assuming QE scattering in mean field potential:
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
nucleon momentum inside 12C
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5 abs{ vec{p_i} }
pi
ptg
Before Scattering:
p1
p2

---
Momentum components of p_i
After Scattering:
p11B
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
pi Momentum-Components (with angular cuts applied)
z-comp
y-comp
x-comp
size*1.5 abs{ vec{p_i} }
pi
ptg
Before Scattering:
p1
p2

---
Mass reconstuction of p_i
Before Scattering:
After Scattering:
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
p1
ptg
pi
size*1.5{M_i = sqrt{(bold{p_1} + bold{p_2} - bold{p_tg})^2} }
p11B
p2
Looks ok, mean of 918 MeV is lower than expected….

---
Missing Energy Distribution
Definition of Missing Energy *:
(where e_miss is the energy component of pmissing)
Emiss = - (Efinal – Einitial)
size*1.5{E_miss " " = " " m_p - e_miss " " = " " E_tgkin - E_p1kin - E_{p2kin} }
( in 12C cms )
color gray size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
Cuts: θ1 + θ2 < 90° and Δφ = 180° +- 40°
But how can this prominent edge be explained?
Emiss = ESep + EExc
*From: https://www.nature.com/articles/s41567-021-01193-4.pdf

---
Analysis Missing Energy Distribution
Explicit calculation of the Missing Energy (in the 12C frame):
Emiss = Etgkin - Ep1kin – Ep2kin
size*1.2{ E_miss = 400 - ( %gamma*(E_kin1+938) - %gamma*%beta*sqrt{(E_kin1+938)^2 -938^2}*cos(%theta_1) -938 ) - ( %gamma*(E_kin2+938) - %gamma*%beta*sqrt{(E_kin2+938)^2 -938^2}*cos(%theta_2) -938 )}
E_potp1
E’p1
E_potp2
E’p2
Etgkin
Ekin2
Ekin1

---
E_missing and p_z_missing for different opening angles
For simplicity let’s say θ1 = θ2. That means for theta_sum = 44 ° → θ1 = θ2 = 22°
Maximum ≈ 270 MeV

---
E_missing and p_z_missing for θ1 = θ2 = 42°
Quasi-Free Scattering reaction
 ≈ 84°

---
Momentum components of p11B
Before Scattering:
After Scattering:
p1
ptg
size*1.5 abs{ vec{p_i} }
pi
p11B
p2
p11B Momentum-Components (with angular cuts applied)

---
Inner angular distributions
pi determined by angle and energy deposition of p1 and p2
p11B determined by ToF and tracking detectors (MWPCs)
(p11B_y was calculated by y-position in MW1 and MW2)
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
Not satisfactory….
See: https://www.nature.com/articles/s41567-021-01193-4.pdf
Here I plotted the angle between the 3D vectors pi and p11B
This is the angle in the x-y plane

---
Angular Distribution in x-y plane
Therefore the y position was determined using MWPC3
(larger lever arm)
The y-position of MWPC3 has been reversed (+y→-y and -y→+y)
Moreover:
* MW0X inverted
* MW1Y and MW2Y swapped

---
Correlation between knocked out proton and 11B
Assuming no inner momenta of the 12C constituents pi and p11B:
→ scattering would take place in reaction plane defined by p12C and p’tg
p’i
p’tg
ptg
pi
p11B
With given formula:
p11B
Reaction plane

---
Correlation between knocked out proton and 11B
Assuming no inner momenta of the 12C constituents pi and p11B:
→ scattering would take place in reaction plane defined by p12C and p’tg
BUT:
→ there are components perpendicular to the reaction plane!
p’i
size*1.5 {abs{ vec{p_i}} approx abs{vec{p_11B} } <> 0 }
p’tg
ptg
pi
p11B
With given formula:
p11B
Reaction plane

---
Correlation between knocked out proton and 11B
This is with Py_fragment reconstruction from MW1 and MW3
With given formula:

---
Correlation between knocked out proton and 11B
What we expect:
experiment
simulation

---
Momentum p_i vs p_11B in 12C
With y-information from MW1 and MW2
Now with y-info from MW1 and MW3
p_x ≈ p_y

---
Missing mass reconstruction
pi
p1
p2
ptg
11B
size*1.5{M_miss = sqrt{(p_12C - p_i - p_11B)^2} }
11B
should be ≈ 0
→ give better look at the 3- momentum distribution
(+- permutation at MW position??)
→ as the reconstruction of p_i works well it can be deduced that 11B reconstruction faulty….
???
size*1.5 abs{ vec{p_i} }

---
Excitation Energy of 11B
size*2{ E_exc = (bold{P_12C + p_tg - p_1 -p_2}).M -M_11B }
-pi
Is this formula valid?

---
Explanation of
Is a Cartesian component of the internal momentum of the internal momentum of the knocked out proton from 12C perpendicular to the reaction plane.
The reaction plane is given by the 12C momentum vector and the scattered target proton.
Can be plotted also against Px_fragment (see next slide). This is a blurred centered spot. This can be explained by:
→ acceptance of CALIFA: no crystals in the phi +-90° region , therefore the y component is dominant
→ low precision for y position (can be partly solved using MW1.Y vs MW3.Y, but then straggling..)
For more details and derivation see: https://www.sciencedirect.com/science/article/abs/pii/S0375947405008523

---
12C(p,ppn/pd)10B Reaction
or

---
First Angular and Momentum Plots ...
Without cut:

---
Reconstruction of inner momentum p_i
size*1.5 {abs{ vec{p_i} } " " (MeV/c)}
size * 1.5 {bold{p_{ i }} = ( bold{p_{1} + p_{1} - p_tg } )}

---
Neutron Mass Reconstruction
???
before reaction
after reaction
size * 1.5 {M²_{ missing } = ( bold{p_{12C} + p_{tg} - p_1 - p_2 - p_{10B}} )^2}