Quasi Free Scattering Analysis with Experiment S444/467 (2020)
12C(p,2p)11B reaction:
SETUP:
Beam energy: 400 AMeV
Beamtype: 12C
Target: CH2
2 protons
11B fragment
(spectator)
12C beam
proton like target
proton
11B
proton

---
Fragment Particle Identification
Flightpath reconstruction:
12C
11C
Radius reconstruction:
size*1 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
10B
11B
size*1.5 {B*%rho " " = " "{{%beta*%gamma*M} over {q}}}

---
12C(p,2p)11B reaction
Two Proton Identification:
→ two hits with Ehit > 30 MeV
proton
proton

---
Gamma Spectrum of 11B
laboratory system
Doppler Correction:
size*1.5 E_{ %gamma } = size*1.5 %gamma size*1.5E_{ lab} size*1.5( 1- %beta cos (%theta ))
11B rest frame
2.1 MeV (1/2-) p-hole state
5.0 MeV (3/2-) p-hole state
+ single/double escape

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
y
φ
x
φ1[degrees]
Tobias Jenegger
φ2[degrees]

---
Gamma Spectrum with Angular Cuts
Event selection criteria for CALIFA:
→ 11B fragment identification
→ two hits (protons) with Ehit > 30 MeV
→ θ1 + θ2 < 90°
→ Δφ = 180° +- 40°
TODO: make bkg from 1 to 3 and add also plots with hit-multiplicities...

---
Reconstruction of Inner Momenta
pi
p1
p2
ptg
11B
11B
Momentum conservation relation:
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
assuming QE scattering in mean field potential:
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
nucleon momentum inside 12C
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5 abs{ vec{p_i} }

---
Momentum components of p_i
pi
p1
p2
Momentum conservation relation:
ptg
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
11B
assuming QE scattering in mean field potential:
11B
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
z-component (with cuts applied)
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
TO DO: x and y component with cut!
size*1.5 abs{ vec{p_i} }

---
Missing Energy Distribution
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5{E_miss " " = " " m_p - e_miss (" "approx E_kin ) }
11B
(where e_miss is the energy component of pmissing)
pi
ptg
11B
p2
p1

---
Mass reconstuction of p_i
pi
p1
p2
ptg
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5{M_i = sqrt{(bold{p_1} + bold{p_2} - bold{p_tg})^2} }
11B
11B
Looks ok, mean of 918 MeV is lower than expected….
size*1.5 abs{ vec{p_i} }

---
Missing mass reconstruction
pi
p1
p2
ptg
11B
size*1.5{M_miss = sqrt{(p_12C - p_i - p_11B)^2} }
11B
should be ≈ 0
→ give better look at the 3- momentum distribution
(+- permutation at MW position??)
→ as the reconstruction of p_i works well it can be deduced that 11B reconstruction faulty….
???
size*1.5 abs{ vec{p_i} }

---
Inner angular distributions
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
In 12C cms frame:
Not satisfactory….
See: https://www.nature.com/articles/s41567-021-01193-4.pdf

---
12C(p,ppn/pd)10B Reaction
or

---
First Angular and Momentum Plots ...
Without cut:

---
Reconstruction of inner momentum p_i
size*1.5 abs{ vec{p_i} }
size * 1.5 {bold{p_{ i }} = ( bold{p_{1} + p_{1} - p_tg } )}

---
Neutron Mass Reconstruction
Making cut on the reconstructed neutron:
???
size * 1.5 {M²_{ missing } = ( bold{p_{12C} + p_{tg} - p_1 - p_2 - p_{10B}} )^2}

---
Summary & Outlook
→ further investigations for the 12C(p,ppn/pd)10B reaction channel needed
→ promising first analysis results from 12C(p,2p)11B
     reconstruction
→ looking forward to exciting upgrade of CALIFA filling the Barrel (backward)
region and the most forward CEPA region

---
Thank you!
CALIFA @ Technical University of Munich (TUM)
Roman Gernhäuser, Lukas Ponnath, Philipp Klenze, Tobias Jenegger
Thank you!

---
Backup