Quasi Free Scattering with S444 Data (2020)
Tobias Jenegger
Analysis WG Meeting
22.07.2021
12C(p,2p)11B reaction
12C(p,ppn/pd)10B reaction
SRC Analysis
Supported by BMBF 05P15WOFNA and 05P19WOFN1.
The results presented here are based on the experiment s444/s473, which was performed at the beam line/infrastructure Cave C at the GSI Helmholtzzentrum für Schwerionenforschung, Darmstadt (Germany) in the frame of FAIR Phase-0.
Physics with R3B
CALIFA – Design

---
Quasi Free Scattering Analysis with Experiment S444/467 (2020)
12C(p,2p)11B reaction:
SETUP:
Beam energy: 400 AMeV
Beamtype: 12C
Target: CH2
2 protons
11B fragment
(spectator)
12C beam
proton like target
proton
11B
proton

---
Fragment Particle Identification
Flightpath reconstruction:
12C
11C
Radius reconstruction:
size*1 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
10B
11B
size*1.5 {B*%rho " " = " "{{%beta*%gamma*M} over {q}}}

---
12C(p,2p)11B reaction
Two Proton Identification:
→ two hits with Ehit > 30 MeV
proton
proton

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
y
φ
x
φ1[degrees]
Tobias Jenegger
φ2[degrees]

---
Gamma Spectrum of 11B
laboratory system
Doppler Correction:
size*1.5 E_{ %gamma } = size*1.5 %gamma size*1.5E_{ lab} size*1.5( 1- %beta cos (%theta ))
11B rest frame
2.1 MeV (1/2-) p-hole state
5.0 MeV (3/2-) p-hole state
+ single/double escape

---
Gamma Spectrum with Angular Cuts
Event selection criteria for CALIFA:
→ 11B fragment identification
→ two hits (protons) with Ehit > 30 MeV
→ θ1 + θ2 < 90°
→ Δφ = 180° +- 40°

---
Reconstruction of Inner Momenta
After Scattering:
(Four-)Momentum conservation relation:
p11B
size*1.5{bold{p_12C} + bold{p_tg} " " = " " bold{p_1} + bold{p_2} + bold{p_11B}}
assuming QE scattering in mean field potential:
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
nucleon momentum inside 12C
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
size*1.5 abs{ vec{p_i} }
pi
ptg
Before Scattering:
p1
p2

---
Momentum components of p_i
After Scattering:
p11B
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
pi Momentum-Components (with angular cuts applied)
z-comp.
y-comp.
x-comp.
size*1.5 abs{ vec{p_i} }
pi
ptg
Before Scattering:
p1
p2

---
Mass reconstuction of p_i
Before Scattering:
After Scattering:
size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
p1
ptg
pi
size*1.5{M_i = sqrt{(bold{p_1} + bold{p_2} - bold{p_tg})^2} }
p11B
p2
Looks ok, mean of 918 MeV is lower than expected….

---
Missing Energy Distribution
Definition of Missing Energy *:
(where e_miss is the energy component of pmissing)
Emiss = - (Efinal – Einitial)
size*1.5{E_miss " " = " " m_p - e_miss " " = " " E_tgkin - E_p1kin - E_{p2kin} }
( in 12C cms )
color gray size*1.5{bold{p_i} approx bold{p_missing} " " = " " bold{p_1} + bold{p_2} - bold{p_tg} (no ISI/FSI)}
Cuts: θ1 + θ2 < 90° and Δφ = 180° +- 40°
But how can this prominent edge be explained?
Emiss = ESep + EExc
*From: https://www.nature.com/articles/s41567-021-01193-4.pdf

---
Analysis Missing Energy Distribution
Explicit calculation of the Missing Energy (in the 12C frame):
Emiss = Etgkin - Ep1kin – Ep2kin
size*1.2{ E_miss = 400 - ( %gamma*(E_kin1+938) - %gamma*%beta*sqrt{(E_kin1+938)^2 -938^2}*cos(%theta_1) -938 ) - ( %gamma*(E_kin2+938) - %gamma*%beta*sqrt{(E_kin2+938)^2 -938^2}*cos(%theta_2) -938 )}
E_potp1
E’p1
E_potp2
E’p2
Etgkin
Ekin2
Ekin1

---
E_missing and p_z_missing for different opening angles
For simplicity let’s say θ1 = θ2 and Ekin1 = Ekin2. That means for theta_sum = 44 ° → θ1 = θ2 = 22°
Maximum ≈ 270 MeV

---
E_missing and p_z_missing for θ1 = θ2 = 42°
Quasi-Free Scattering reaction
 ≈ 84°

---
Momentum components of p11B
Before Scattering:
After Scattering:
p1
ptg
pi
Spectator!
p11B
p2
p11B Momentum-Components (with angular cuts applied)
y-comp.
x-comp.
z-comp.

---
Inner angular distributions
pi determined by angle and energy deposition of p1 and p2
p11B determined by ToF and tracking detectors (MWPCs)
(p11B_y was calculated by y-position in MW1 and MW2)
size*1.5{bold{p_12C} " " = " " bold{p_i} + bold{p_11B}}
Not satisfactory….
See: https://www.nature.com/articles/s41567-021-01193-4.pdf
Here I plotted the angle between the 3D vectors pi and p11B
This is the angle in the x-y plane

---
Angular Distribution in x-y plane
Therefore the y position was determined using MWPC3
(larger lever arm)
The y-position of MWPC3 has been reversed (+y→-y and -y→+y)
Moreover:
* MW0X inverted
* MW1Y and MW2Y swapped

---
Spatial Correlation of the Reaction Products
Assuming no inner momenta of the 12C constituents pi and p11B:
→ scattering would take place in reaction plane defined by p12C and p’tg
p1
p2
ptg
pi
p11B
p11B
Reaction plane

---
Spatial Correlation of the Reaction Products
Assuming no inner momenta of the 12C constituents pi and p11B:
→ scattering would take place in reaction plane defined by p12C and p1/2
BUT:
→ there are components perpendicular to the reaction plane!
p1
size*1.5 {abs{ vec{p_i}} approx abs{vec{p_11B} } <> 0 }
p2
ptg
pi
p11B
p11B
Reaction plane

---
Spatial Correlation of the Reaction Products
As measure of the overall perpendicular fraction to the reaction plane*:
(vec{p_2} x vec{p_12C})
vec p_1
size*1.5{Q_tr12 " " = " " abs{{vec{p_1}}} {vec{p_1}*(vec{p_2} x vec{p_12C}) over {abs{vec{p_1}}abs{vec{p_2} x vec{p_12C}}}}}
Q_tr12
vec p_12C
vec p_2
or
vec p_1
vec p_12C
size*1.5{Q_tr21 " " = " " abs{{vec{p_2}}} {vec{p_2}*(vec{p_1} x vec{p_12C}) over {abs{vec{p_2}}abs{vec{p_1} x vec{p_12C}}}} " " = " " - Q_tr12}
-Q_tr12
vec p_2
(vec{p_1} x vec{p_12C})
Due to momentum conservation:
size*2{ Q_tr12 " " = " " - Q_trFragment }
*Further details: https://www.sciencedirect.com/science/article/abs/pii/S0375947405008523

---
Qtr12 vs. |p_y11B|
Qtr12 / Qtr21

---
Qtr12 vs. |p_y11B|
Qtr12
Qtr21
Qtr12 / Qtr21

---
Qtr12 vs. |p_x11B|
due to restricted geom. acceptance in iPhos region
Qtr12 / Qtr21

---
Momentum p_i vs p_11B in 12C
in 12C frame

---
Missing Mass Reconstruction
size*1.5{M_miss = sqrt{(bold{p_12C + p_tg -p_1 - p_2 - p_11B})^2} }
( should be ≈ 0 )
???
before scattering
after scattering
p1
ptg
p11B
p12C
p2
size*1.5 abs{ vec{p_i} }

---
12C(p,ppn/pd)10B Reaction
12C(p,pd)10B:
Short-Range-Correlated (SRC) Pair:
- possible explanation for the EMC – effect
- nucleon pairs with high relative and low c.m. momentum (compared to Fermi momentum kF)
Neutron Evaporation:

---
First (Polar) Angular Plots ...
θ1(proton 1) vs. θ2 (proton2) without any angular restrictions:
Constraints:
E1lab and E2lab > 30MeV
Identification of 10B
θ1[°]
θ2[°]

---
First (Polar) Angular Plots ...
θ1(proton 1) vs θ2 (proton2) without any angular restrictions:
Full Acceptance in Barrel Region
θ1[°]
θ2[°]

---
First (Polar) Angular Plots ...
θ1(proton 1) vs θ2 (proton2) without any angular restrictions:
???
Full Acceptance in Barrel Region
θ1[°]
θ2[°]

---
First (Polar) Angular Plots ...
θ1(proton 1) vs θ2 (proton2) without any angular restrictions:
      Cluster algoritm:
CalifaCal2Hit->SetConeAlg(0.25)
θ1[°]
θ2[°]

---
First (Polar) Angular Plots ...
θ1(proton 1) vs θ2 (proton2) with angular cut: Δφ > 100°
θ1[°]
θ2[°]

---
Reconstruction of inner momentum p_i
size*1.5 {abs{ vec{p_i} } " " (MeV/c)}
size * 2 bold{vec{p_i} = vec{ p_1 } + vec{ p_2 } - vec{ p_tg }}
size*1.5 bold{abs{ vec{p_i} } " " < " " 250} size*1.5 bold{250 " " < " "abs{ vec{p_i} } " " < " " 650} size*1.5 bold{650 " " < " "abs{ vec{p_i} } }

---
Angular Distribution for |p_i| < 250
θ1[°]
θ2[°]
size*1.5 bold{abs{ vec{p_i} } " " < " " 250} size*1.5 bold{250 " " < " "abs{ vec{p_i} } " " < " " 650} size*1.5 bold{650 " " < " "abs{ vec{p_i} } }

---
Angular Distribution for 250 MeV/c < |p_i| < 650 MeV/c
θ1[°]
size*1.5 bold{abs{ vec{p_i} } " " < " " 250} size*1.5 bold{250 " " < " "abs{ vec{p_i} } " " < " " 650} size*1.5 bold{650 " " < " "abs{ vec{p_i} } }
θ2[°]

---
Angular Distribution for |p_i| > 650 MeV/c
θ1[°]
size*1.5 bold{abs{ vec{p_i} } " " < " " 250} size*1.5 bold{250 " " < " "abs{ vec{p_i} } " " < " " 650} size*1.5 bold{650 " " < " "abs{ vec{p_i} } }
θ2[°]

---
Neutron Mass Reconstruction
size * 1.5 {M²_{ missing } " " = " "( bold{p_{12C} + p_{tg} - p_1 - p_2 - p_{10B}} )^2 " " approx m_n }
after reaction
before reaction
???
Possible Explanations:
→ boosting effects
→ biased z-momenta
→ further checks needed

---
To do:
Angular correlations fo the proton and reconstructed neutron
Angular correlation of src pair and 10B
Tobias Jenegger

---
Summary & Outlook
12C(p,2p)11B Quasi Free Scattering looks promising
But: Momentum shift in z-direction has to be further analyzed
For 12C(p,ppn/pd)10B already first results
How to distinguish between the three reaction types? (Deuteron detection with Nf-Ns information from CALIFA? Reasonable cuts?)
Deuteron Knockout
SRC - pair
Neutron Evaporation

---
Backup

---
Excitation Energy of 11B
size*2{ E_exc = (bold{P_12C + p_tg - p_1 -p_2}).M -M_11B }
-pi
Is this formula valid?

---
Excitation Energy vs. E_miss
Excitation Energy [MeV]